## Slide 1
NORTHEASTERN UNIVERSITY · EECE 5642 DATA VISUALIZATION
Visual
Profiling
of KITTI Odometry Sequences
Multi-Metric Difficulty Visualization & Cluster Analysis
SYED HAMED ALI
11
Sequences
7
Metrics
94.3%
PCA Var.
k=3
Clusters

## Slide 2
02
WHAT IS SLAM?
2
Simultaneous Localization and Mapping — the core challenge in autonomous navigation
🤖
SLAM answers: "Where am I?" and "What does the world around me look like?" — simultaneously, in real time, from noisy sensors.
01
🔄
The Circular Dependency
To build a map, you need to know where you are. But to know where you are, you need a map.
Formally: p(xₜ, m | z₁:ₜ, u₁:ₜ) — estimating pose and map jointly from sensor data.
02
📈
Trajectory Drift
Every sensor reading has noise. Small per-frame errors compound over time. A robot driving 2km can end up 100m from its true position.
This is the PRIMARY difficulty metric in our analysis.
03
🔁
Loop Closure
When a robot revisits a known location, SLAM corrects accumulated drift — recognizing landmarks. This is why urban sequences (turns, loops) have LOWER drift than straight highway routes.
Seq 01 has NO loop closure → 1,980m drift.
04
🚗
Why It Matters
SLAM is the backbone of every autonomous vehicle, drone, and mobile robot. Tesla Autopilot, Waymo, Boston Dynamics, Mars rovers — ALL rely on SLAM. Getting benchmarking right advances the entire field.

## Slide 3
03
WHY KITTI?
3
The world's most important autonomous driving benchmark — and why researchers rely on it
🏆 What Makes KITTI Special
✅ Real-world complexity — not simulation
✅ Diverse environments: urban, highway, campus
✅ Standardized t_err / r_err evaluation protocol
✅ Fair comparison across all published algorithms
✅ Free & open-access since 2012
✅ Ground truth from GPS/IMU — not from vision
✅ 10,000+ papers cite KITTI (Google Scholar)
Why Researchers Choose KITTI
📅 Year:
2012 — Geiger et al., KIT, Germany
🚗 Platform:
VW Passat with full sensor suite
📷 Cameras:
Stereo grayscale, 10Hz, 1.4MP
📡 LiDAR:
Velodyne HDL-64E, 10Hz, 64 beams
🌐 GPS/IMU:
RTK — centimeter-level ground truth
📐 How Pose Files Work
Each line = 1 frame = 12 numbers:
[ R R R Tx ] [ R R R Ty ] [ R R R Tz ]
→ R=rotation matrix · T=translation (X,Y,Z per frame)

## Slide 4
04
THE PROBLEM
4
Why standard benchmarking tables fail multi-metric analysis
❓
"Which KITTI sequence is hardest — and WHY?" · 7 metrics × 11 sequences = 77 numbers. A table cannot answer this. Visualization can.
01
🔢
Information Overload
11 sequences × 7 metrics = 77 numbers per comparison. Human working memory handles ~7 items. Tables create cognitive overload before any insight can form.
02
🔍
Clusters Are Invisible
Natural Easy/Medium/Hard groupings exist in the data — but no table can reveal them. Visualization with K-Means clustering makes them immediately legible.
03
📊
Redundancy Undetectable
Accum. Drift and Late Error have r=0.95 correlation. A table never reveals this. The heatmap shows it as a single bright cell.
04
⏱
Temporal Patterns Hidden
Whether error grows early or late in a sequence changes algorithmic interpretation completely. This dimension is invisible in summary statistics.
05
⚡
Outliers Blend In
Seq 01 (0.793) and Seq 04 (0.137) differ by 5.8×. In a sorted column Seq 01 is just "the highest number." In a bar chart its exceptionality is unmistakable.
06
🧩
No Geometric Context
Summary statistics cannot show that Seq 01's high drift is caused by straight-line driving with zero turns. Trajectory plots reveal this physical cause instantly.

## Slide 5
05
DATA VISUALIZATION IN CONTEXT
5
Every data-driven field reaches its limits without visualization — here is why
💡
Visualization is not a reporting tool — it is the scientific bridge between raw data and human understanding, essential in every data-driven discipline.
ML
🤖
Machine Learning
Loss curves, confusion matrices, feature importance — all invisible as raw numbers. Visualization reveals overfitting, bias, and model behavior in seconds.
CV
👁
Computer Vision
Bounding boxes, attention maps, segmentation masks — the core outputs of CV models are inherently spatial. They MUST be visualized to be evaluated.
DS
📊
Data Science
Anscombe's Quartet proved it in 1973: identical summary statistics can describe completely different datasets. Plots reveal what numbers hide.
RL
🎮
Reinforcement Learning
Reward trajectories, policy maps, value functions — understanding agent behavior requires animated trajectories and heatmaps, never just scalars.
NLP
💬
Natural Language / LLMs
Embedding spaces, attention weights, token probability distributions — transformer internals only become interpretable through dimensionality reduction and heatmaps.
🤖
🚗
Robotics & SLAM
Trajectory drift, map quality, loop closure events — this is OUR domain. Standard tables hide the structure that our visualizations expose.

## Slide 6
06
OBJECTIVES
6
Six goals — each addressing a gap in current benchmarking practice
O1
📐
Extract Difficulty Features
Compute 7 heterogeneous metrics from raw KITTI pose files — RMSE, drift slope, accumulated drift, early/late error, curvature, entropy — no estimated trajectory required.
O2
🔵
Cluster into Difficulty Tiers
Apply K-Means (k=3) to objectively separate sequences into Easy, Medium, Hard tiers. Validate with silhouette coefficient ≈ 0.61, optimal over k=2–5.
O3
📈
Reveal Hidden Patterns
Design 5 complementary visualizations each revealing one finding invisible in tables: radar, heatmap, PCA scatter, ranked bars, runtime scatter.
O4
🔬
Argue for Visual Analytics
Demonstrate with Anscombe's Quartet logic that 4 of 6 key benchmarking questions are unanswerable from tabular data. Visualization is science, not decoration.
O5
✅
Validate the Metric Set
Confirm via PCA that 7 metrics explain 94.3% of difficulty variance in 3 components — proving the feature set is complete and minimally redundant.
O6
🌍
Build Transferable Tools
Deliver open-source Python pipeline + interactive HTML dashboard applicable to EuRoC, TUM-RGBD, or any ground-truth pose dataset worldwide.

## Slide 7
07
DATASET OVERVIEW
7
11 KITTI sequences — real ground-truth poses from instrumented vehicle
🚗 Sensor Suite
📷 Cameras:
Stereo grayscale, 1.4MP, 10Hz, B=0.54m baseline
📡 LiDAR:
Velodyne HDL-64E, 64 beams, 10Hz, 360°
🌐 GPS/IMU:
RTK-GPS ±2cm accuracy — centimeter ground truth
🚘 Vehicle:
VW Passat, up to 90 km/h
📊 Sequences:
11 training (labeled 00–10)
🗺️ Total:
22,202 frames total
📐 Format:
3×4 SE(3) matrix per frame
⚙️ GT Method:
GPS/LiDAR/IMU fusion
Sequence Frames & Difficulty — Real Computed Values
Seq
Frames
Score
Cluster
Seq 00
4,541
0.258
Medium
Seq 01
1,101
0.793
Hard
Seq 02
4,661
0.444
Medium
Seq 03
801
0.222
Easy
Seq 04
271
0.137
Easy
Seq 05
2,761
0.274
Medium
Seq 06
1,101
0.171
Easy
Seq 07
1,101
0.355
Medium
Seq 08
4,071
0.276
Medium
Seq 09
1,591
0.271
Medium
Seq 10
1,201
0.333
Medium
← Frames
Score →
Easy (3 seqs)
Medium (7 seqs)
Hard (1 seq)

## Slide 8
08
METHODOLOGY
8
5-step pipeline: raw poses → metrics → clusters → visualizations
01 Load Poses
📂
Read KITTI .txt files
3×4 SE(3) matrices
Extract XYZ translation
Per-frame positions
▶
P = [R|t]
02 7 Metrics
📐
RMSE · Drift Slope
Accum. Drift
Early + Late Error
Curvature · Entropy
▶
κ, H, σ(Δt)
03 Normalize
⚖️
Min-Max → [0,1]
Equal weighting
Unit-independent
Composite score
▶
m̂=(m−min)/(max−min)
04 K-Means k=3
🔵
Easy / Medium / Hard
20 random restarts
Fixed seed=42
Silhouette ≈ 0.61
▶
argmin Σ||x−μ||²
05 Visualize
📊
Radar · Heatmap
3D PCA Scatter
Ranked Bars
Runtime Scatter
5 charts × 1 insight
⚡ Algorithm-agnostic: works with ANY ground-truth pose dataset — EuRoC · TUM-RGBD · Newer College · Custom deployment

## Slide 9
09
VISUALIZATION 1 — RADAR CHART
9
See all 7 metrics for all 3 clusters simultaneously — impossible from a table
Chart: 
| RMSE | Drift Slope | Accum.Drift | Early Err | Late Err | Curvature | Entropy
Easy | 0.12 | 0.14 | 0.08 | 0.09 | 0.07 | 0.13 | 0.1
Medium | 0.41 | 0.18 | 0.35 | 0.38 | 0.4 | 0.48 | 0.55
Hard | 0.79 | 1 | 1 | 0.98 | 0.95 | 0.05 | 0.4
🟢 Easy Cluster
Uniformly flat across all 7 axes — all metrics near zero. Short paths (Seq 03, 04, 06) with simple geometry and low drift. Ideal for algorithm development and debugging.
🟡 Medium Cluster
Moderate polygon with elevated entropy from urban turns and diverse headings. 7 sequences span 0.258–0.444. High heterogeneity suggests further sub-clustering may be valuable.
🔴 Hard Cluster — Seq 01 ONLY
Extreme asymmetric profile: maximum on Drift Slope, Accum. Drift, Early/Late Error, RMSE — but near-ZERO on Curvature (0.005). Physical signature of straight highway: no turns = no loop closure = 1,980m drift.
💡 This single chart replaces 3 table columns and reveals cluster structure the table hides.

## Slide 10
10
VISUALIZATION 2 — CORRELATION HEATMAP
10
Pearson r between all metric pairs — discovering redundancy and independence
RMSE
Drift
Accum.
Early
Late
Curv.
Entr.
RMSE
Drift
Accum.
Early
Late
Curv.
Entr.
1.00
0.32
0.62
0.56
0.70
0.12
0.29
0.32
1.00
0.78
0.33
0.78
-0.26
-0.62
0.62
0.78
1.00
0.76
0.95
★
-0.31
-0.18
0.56
0.33
0.76
1.00
0.80
-0.30
0.36
0.70
0.78
0.95
★
0.80
1.00
-0.29
-0.06
0.12
-0.26
-0.31
-0.30
-0.29
1.00
0.28
0.29
-0.62
-0.18
0.36
-0.06
0.28
1.00
r = 0.95
HIGH IMPACT
Accum. Drift ↔ Late Error
Near-REDUNDANT — same phenomenon captured twice. One metric can be dropped from future benchmarks without information loss.
r = −0.62
PHYSICAL INSIGHT
Drift Slope ↔ Entropy
INVERSE — urban routes with diverse headings self-correct via near-loop-closure events, reducing linear drift accumulation.
r = 0.12
KEEP BOTH
RMSE ↔ Curvature
Nearly INDEPENDENT — these metrics capture orthogonal difficulty dimensions. Both must be retained for a complete evaluation.
-1.0 -0.5 0 +0.5 +1.0

## Slide 11
11
VISUALIZATION 3 — DIFFICULTY RANKING
11
Composite scores ranked — revealing the shocking gap at the top
Chart: 
| Seq 04 | Seq 06 | Seq 03 | Seq 09 | Seq 07 | Seq 00 | Seq 05 | Seq 08 | Seq 10 | Seq 02 | Seq 01
Difficulty Score | 0.137 | 0.171 | 0.222 | 0.271 | 0.355 | 0.258 | 0.274 | 0.276 | 0.333 | 0.444 | 0.793
🔴 Seq 01: CATEGORICAL OUTLIER
Score 0.793 — the ONLY Hard sequence.
Gap to next: 0.349 (> entire Medium spread 0.186).
Cause: straight highway, zero turns, zero loop closure.
→ Not "just hard" — a different category of issue.
🟠 Medium: Wide Spread
7 sequences, scores 0.258–0.444.
Seq 02 (0.444) nearly 3× harder than Seq 00 (0.258).
High heterogeneity suggests further sub-clustering.
→ "Medium" is a heterogeneous group.
🟢 Easy: Tight Cluster
3 sequences, scores 0.137–0.222.
Seq 04 = simplest: 271 frames, low entropy.
Seq 01 is 5.8× harder than Seq 04.
→ Ideal for algorithm development.

## Slide 12
12
VISUALIZATIONS 4 & 5 — PCA + TEMPORAL DYNAMICS
12
3D cluster separation & error growth patterns across all sequences

## Slide 13
13
VISUALIZATIONS 4 & 5 — PCA + TEMPORAL DYNAMICS
12
3D cluster separation & error growth patterns across all sequences
3-D PCA — 94.3% Variance Explained
PC1
53.9%
Loads: Drift Slope · Accum. Drift · Late Error
→ PRIMARY difficulty axis
PC2
26.6%
Loads: Curvature · Entropy · RMSE
→ PATH GEOMETRY axis
PC3
13.8%
Loads: Early Error · Late Error ratio
→ TEMPORAL GROWTH axis
!
Seq 01 is SPATIALLY ISOLATED in PC1 — not just "the hardest" — a qualitatively different failure mode.
3 Temporal Error Patterns
Pattern 1: MONOTONIC GROWTH
Sequences: Seq 01, 03, 10
Distance from start increases continuously — no return. Algorithm never gets to correct errors. Seq 01 reaches 2,000+ meters.
Pattern 2: OSCILLATING
Sequences: Seq 00, 02, 05, 08, 09
Multiple peaks and valleys — complex urban routes with partial loop returns. Error grows, shrinks, grows again, reflecting city road loops.
Pattern 3: V-SHAPE RETURN
Sequences: Seq 06, 07
Distance rises then returns near zero — near-complete loop closure. Vehicle returns to its starting area, correcting drift geometrically.
💡 The SAME accumulated drift number can arise from all 3 patterns — summary statistics hide this completely.

## Slide 14
14
KEY INSIGHTS & PATTERNS
13
Four discoveries that only visualization could reveal
F1
Seq 01 is Categorically Hard
0.793
vs 0.137 (Seq 04)
The ONLY Hard sequence. 1,980m accumulated drift — caused by straight-line, high-speed highway driving with near-zero curvature (0.005) and no loop closure. Score is 5.8× higher than the easiest. The gap to Seq 02 (0.349) exceeds the entire Medium cluster spread.
💡 Bar chart immediately shows this — a table buries it among 10 other numbers.
F2
Two Metrics Are Redundant
r = 0.95
Accum. Drift ↔ Late Error
These two standard evaluation metrics capture essentially the same phenomenon (Pearson r=0.95). Future benchmarks could safely drop one — reducing researcher burden without any information loss. Direct implication for streamlining KITTI evaluation protocol.
💡 Invisible without the heatmap — the r=0.95 bright red cell is unmistakable.
F3
Runtime ≠ Difficulty
r = −0.045
p = 0.895 (not significant)
Processing time has near-zero correlation with difficulty score (r=−0.045, p=0.895). Runtime is driven entirely by frame count (r≈0.97). Hard sequences are NOT slower to process — they're harder for the algorithm, not the computer. Computational budgeting by difficulty tier would be misguided.
💡 Only the runtime scatter reveals this counterintuitive non-relationship.
F4
Metric Set is Complete
94.3%
Variance in 3 PCA dims
Three PCA components explain 94.3% of all difficulty variance: PC1=drift (53.9%), PC2=geometry (26.6%), PC3=temporal (13.8%). This validates our 7-metric framework as comprehensive — no important difficulty dimension is missing, and dimensionality reduction is fully justified.
💡 Only PCA scatter reveals the dimensionality structure of difficulty space.

## Slide 15
15
COMPARATIVE ANALYSIS
14
Table vs. Visualization — a scientific argument for visual analytics
Research Question
From Raw Table
From Our Visualizations
Which sequence is hardest?
❌ Scan 11 numbers manually — 10+ sec
✅ Fig.11 ranked bar: Seq 01 bar is 5.8× longer — 0.3 sec
Are any metrics redundant?
❌ Impossible — need 21 Pearson computations
✅ Fig.10 heatmap: r=0.95 bright cell — instant
Do clusters exist?
❌ Impossible — need clustering algorithm
✅ Fig.12 PCA: 3 groups spatially separated — visible
Does harder = slower to process?
❌ Cannot determine from scores alone
✅ Runtime scatter: flat trend, r≈0 — counterintuitive
How does error grow over time?
❌ Completely invisible in summary stats
✅ Temporal chart: 3 qualitatively different patterns
What does the actual path look like?
❌ Completely invisible — no spatial info
✅ Trajectory viewer: geometry and loops legible
Verdict: 4 of 6 research questions are COMPLETELY UNANSWERABLE from raw tabular data. Visualization is not a presentation choice — it is a scientific necessity.

## Slide 16
16
REAL-WORLD IMPACT & APPLICATIONS
15
Six areas where this work changes practice
Industry
Research
Development
🚗
AV Testing
AV test teams can pre-select sequences by difficulty tier, focusing expensive vehicle hours on Hard sequences that expose algorithmic weaknesses.
🎓
Curriculum Learning
Train deep odometry networks ordering KITTI by ascending composite score (0.137→0.793). Easier-first training provably improves convergence.
🔬
Algorithm Debugging
If an algorithm fails only on Seq 01, this framework immediately identifies the cause: loop-closure failure on straight-highway sequences. Saves weeks of debugging.
📏
Metric Pruning
The r=0.95 finding enables dropping Late Error from future KITTI evaluations, reducing overhead while retaining all discriminative information.
🌍
Cross-Dataset
Framework transfers to EuRoC, TUM-RGBD, Newer College with zero modification — any dataset with ground-truth poses can be profiled identically.
📊
Paper Communication
Authors can include a single difficulty radar chart to instantly communicate why their algorithm excels on certain sequences — replacing 3 dense pages of tables.

## Slide 17
NORTHEASTERN UNIVERSITY · EECE 5642 · PROF. Y. RAYMOND FU
C O N C L U S I O N
Visualization transforms
benchmarks into science.
SLAM + KITTI :
Profiled all 11 sequences of the world-standard benchmark using real ground-truth poses
7 Metrics :
Captured error, drift, temporal dynamics, geometric complexity, and heading diversity
Seq 01 Outlier :
Score 0.793 — 5.8× harder than Seq 04 — 1,980m drift — explained by zero curvature
r = 0.95 :
Accum. Drift & Late Error are near-redundant — metric pruning is scientifically justified
94.3% PCA :
7 metrics span difficulty space — validated by 3-component PCA decomposition
Thank You
Questions & Discussion